CH-O-2000-1201                   * CH-O-(0500~3000)-1201 is a Hall-Effect current transducer.

Current Transducer                            * It can be used for the detection of DC, AC, pulse.

| Electrical data |
| --- |
| IPN | Primary nominal r.m.s current |  |  |  | 2000 | A |
| IP | Primary current, measuring range |  |  |  | ( 5000 | A |
| VSN | Rated voltage | ±4 | V |
| VC | Supply voltage (( 5%) | ( 15 | V |
| IC | Idle current consumption | < 30 | mA |
| Vd | AC isolation test, 50 Hz, 1min RM max | 2.5 | kV |
| RIS | Isolation resistance @ 500 VDC 0 22 | > 500 | M( |
| VOUT | Output voltage @ ( IPN, RL = 10 k(, TA = 25(C | 0…( 10 | V |
| RL | Load resistance | ≥ 10 | k( |

| Accuracy – Dynamic performance data |
| --- |
| X | Accuracy @ IPN , TA = 25(C (without offset) | < ( 1 | % |
| (L | Linearity (0.. ( IPN) | ( ( 1 | %of IPN |
| VOE | Electrical offset voltage @ IP = 0, TA = 25(C @(100 Amax 0 0 | < ( 20 | mV |
| VOH | Hysteresis offset voltage @ IP = 0; |  |  |
|  | after an excursion of 3 ( IPN | < ( 30 | mV |
| VOT | Thermal drift of VOE | < ( 1 | mV/℃ |
| tr | Response time @ 90% of IP | < 10 | (s |
| di/dt | di/dt accurately followed | > 50 | A/(s |
| f | Frequency bandwidth (-3 dB) | DC…25 | kHz |

| General data |
| --- |
| TA | Ambient operating temperature |  | -10..+100 | (C |
| m | Mass |  | 280 | g |

Direction of use:

Precaution -	Nominal current measuring range: 500A ~ 3000 A (AC) or 500 A ~ 3000 A (DC).

Output voltage: 0 ~ (10 V.

Or output current:  0～20mA.

If the above-stated condition is fulfilled, go to following steps:

Put the conducting wire through the center hole of the current transducer.

Connected the transducer as the pictures shown.

Adjust the OFS to obtain a zero offset output voltage if offset is non-zero. (EX-Factory is zero offset)

Adjust the GIN to obtain a desire maximum output voltage. (EX-Factory is 4V typical)

# Text boxes

IPN =2000 A

VOUT = 0…(10V

Features

- Hall effect measuring principle.

- Galvanic isolation between primary and secondary circuit.

- Low power consumption.

Applications

- AC motor speed control.

- Static converters for DC motor drives.

- Battery supplied applications.

- Uninterruptible Power Supplies (UPS).

- Power supplies for welding, cable TV and telecommunication applications.

Advantages

- Easy mounting.

- Small size and space savings.

- Only one design for wide current ratings range.

- High immunity against external interference.

- Current overload capability.

- Adjustable output gain.

- Adjustable offset to zero.

##### SECONDARY TERMINALS

TERMINAL +: SUPPLY VOLTAGE + 15V

TERMINAL (: SUPPLY VOLTAGE ( 15V

TERMINAL  OUT : OUTPUT MEASURE

TERMINAL  0	: 0 V

##### Adjustment

OFS	:	Zero offset adjust

GIN	:	Output amplitude adjust